## Slide 1: Continuous-Time Fourier Transform
Prof. Brian L. Evans
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
EE 313 Linear Systems and Signals Fall 2021
Lecture 15 http://www.ece.utexas.edu/~bevans/courses/signals
Textbook: McClellan, Schafer & Yoder, Signal Processing First, 2003

## Slide 2: Linear Systems and Signals Topics
Continuous-Time Fourier Transform – SPFirst Ch. 11 Intro
Domain | Topic | Discrete Time | Continuous Time
Time | Signals | SPFirst Ch. 4 | SPFirst Ch. 2
 | Systems | SPFirst Ch. 5 | SPFirst Ch. 9
 | Convolution | SPFirst Ch. 5 | SPFirst Ch. 9
Frequency | Fourier series | ** | SPFirst Ch. 3
 | Fourier transforms | SPFirst Ch. 6 | SPFirst Ch. 11
 | Frequency response | SPFirst Ch. 6 | SPFirst Ch. 10
Generalized Frequency | z / Laplace Transforms | SPFirst Ch. 7-8 | Supplemental Text
 | Transfer Functions | SPFirst Ch. 7-8 | Supplemental Text
 | System Stability | SPFirst Ch. 8 | SPFirst Ch. 9
Mixed Signal | Sampling | SPFirst Ch. 4 | SPFirst Ch. 12

** Spectrograms (Ch. 3) for time-frequency spectrums (plots) computed the discrete-time Fourier series for each window of samples.
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔

## Slide 3: Continuous-Time Fourier Transform
General definition of the frequency spectrum
  Define a precise notion of bandwidth
Periodic signals (SPFirst Ch. 3)
Linear time-invariant systems (SPFirst Ch. 10)
Continuous-Time Fourier Transform – SPFirst Ch. 11 Intro
  Explain inner workings of communication systems
  Analyze continuous-time linear time-invariant filters
  Continuous-time periodic signals represented as sum of cosines
  Cosine frequencies integer multiples of fundamental frequency
  Fundamental frequency w0 = 2 p / T0; T0 is fundamental period
  Output frequencies are only those present in input

## Slide 4: Continuous-Time Fourier Transform
Forward direction
Continuous-Time Fourier Transform – SPFirst Sec. 11-1
Inverse direction
  Analysis: extracts spectrum information from the signal x(t)
  Synthesis: creates time-domain signal x(t) from its spectral info
Build up transform pairs and properties (pp. 338-339)
  As we did for z-transforms and we’ll do for Laplace transforms
Example continuous-time Fourier transforms
  Dirac delta:
  Delayed Dirac delta:
Impulse response of an ideal delay by T seconds
d(t)
h(t)

## Slide 5: Causal Exponential Signal
Continuous-Time Fourier Transform – SPFirst Sec. 11-4.1
Formula:
Oscillates
Decays if Re{a} > 0
  Magnitude-Phase form
w = -8 : 0.01 : 8;
H = 1 ./ (1 + j*w);
Hmag = abs(H);
Hphase = phase(H);
figure;
plot(w, Hmag);
title('Magnitude Response');
ylim( [-0.0 1.1] );
figure;
plot(w, Hphase);
title('Phase Response');
a = 1
See lecture slide 14-5 for an example when a = 2

## Slide 6: Rectangular Pulse in Time
Continuous-Time Fourier Transform – SPFirst Sec. 11-4.2
0
1
t/2
-t/2
t
x(t)
0
t
w
X(jw)
-6p
t
-4p
t
-2p
t
2p
t
4p
t
6p
t
F
Visualizing Fourier transforms adds insight and guides mathematics

## Slide 7: Impulse in Time or Frequency
From sifting property of Dirac delta,
0
1
t
x(t) = 1
F
(2p) indicates area under Dirac delta
w
X(jw) = 2p d(w)
(2p)
0
Continuous-Time Fourier Transform – SPFirst Sec. 11-4.4
Consider Dirac delta in Fourier domain
  Using linearity property, F{ 1 } = 2p d(w)

## Slide 8: Two-Sided Cosine Signal
X(jw)
0
t
x(t) = cos(w0 t)
F
0
w
w0
-w0
(p)
(p)
Continuous-Time Fourier Transform – SPFirst Sec. 11-4.5

## Slide 9: Duality
0
t
t
X(jt)
-6p
t
-4p
t
-2p
t
2p
t
4p
t
6p
t
Forward/inverse transforms are similar
Continuous-Time Fourier Transform – SPFirst Sec. 11-8
Example: rect(t / t)  t sinc(w t / (2p))
  Apply duality t sinc(t t/(2p))  2 p rect(-w/t)
  rect(·) is even t sinc(t t/(2p))  2 p rect(w/t)
F
0
2p
t/2
-t/2
w

## Slide 10: Scaling
For a  0 and given x(t)  X(jw)
Continuous-Time Fourier Transform – SPFirst Sec. 11-5.1
Extent in time domain is inversely proportional to extent in frequency domain (a.k.a. bandwidth)
  |a| > 1: compress time axis, expand frequency axis
  |a| < 1: expand time axis, compress frequency axis
  x(t) is wider  spectrum is narrower
  x(t) is narrower  spectrum is wider

## Slide 11: Shifting in Time
Shifting in time
Continuous-Time Fourier Transform – SPFirst Sec. 11-7.1
Derivation
  Does not change magnitude of Fourier transform
  Shifts phase of Fourier transform by –w t0 (so –t0 is slope of the linear phase)
  Let u = t – t0, so du = dt and integration limits stay same

## Slide 12: Sinusoidal Amplitude Modulation
Continuous-Time Fourier Transform – SPFirst Sec. 11-8
F
F
Multiplication in time is convolution in frequency
Alternate derivation (SPFirst Sec. 12-2.1)

## Slide 13: Amplitude Modulation by Cosine
y(t) = x(t) cos(wc t)
w
0
Y(jw)
½
-wc - w1
-wc + w1
-wc
wc - w1
wc + w1
wc
½X(j(w - wc))
½X(j(w + wc))
  Assume x(t) is ideal lowpass signal with bandwidth w1 < wc
w
0
1
w1
-w1
X(jw)
What are applications of amplitude modulation?
Continuous-Time Fourier Transform – SPFirst Sec. 11-8

## Slide 14: Amplitude Demodulation by Cosine
How to recover x(t) from y(t) = x(t) cos(wc t) ?
w
0
Y(jw)
½
-wc - w1
-wc + w1
-wc
wc - w1
wc + w1
wc
½ X(j(w - wc))
½ X(j(w + wc))
F{ y(t) cos(wc t) } = ½ Y(j(w + wc)) + ½ Y(j(w – wc))
¼ X(j(w - 2wc))
¼ X(j(w + 2wc))
½ X(jw)
w
0
- 2wc+w1
-w1
-wc
w1
2wc- w1
wc
2wc
-2wc
2wc+w1
-2wc-w1
½
keep
attenuate
attenuate
Continuous-Time Fourier Transform – SPFirst Sec. 11-8

## Slide 15: Time Differentiation Property
Conditions
Continuous-Time Fourier Transform – SPFirst Sec. 11-7.2
Derivation of property: Given f(t)  F(jw)
  f(t)  0 when |t|  
  f(t) is differentiable

## Slide 16: Time Integration Property
15-16
Example

## Slide 17: License Info for SPFirst Slides
McClellan, Schafer &Yoder have released their work under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation
©2003-2016, JH McClellan & RW Schafer
15-17